## Slide 1: Refining Processes

## Slide 2: European Refining Overview
Crude Oil is a broad mix of hydrocarbons, which must be separated and refined prior to commercial use
Molecules range from very light to very heavy
The first process of any refinery is the fractionation of crude into different fractions by distillation
The fractions are characterized by their boiling temperatures
Refineries exploit the different properties of each fraction to produce finished products

## Slide 3: European Refining Overview
Refined products must meet many quality specifications: legal and fit-for-use
Gasoline / Diesel
Jet / Kerosene
Other Gasoils
Heavy Fuel Oil
Sulphur content
Combustion properties
Volatile organic compounds
Density
Flash point
Freeze point
Water content
Sulphur content
Combustion properties
Cold Flow properties
Density
Sulphur content
Viscosity
Density

## Slide 4: European Refining Overview
The processes used by refineries can be classified into four categories
Separation
  Atmospheric distillation
  Vacuum distillation
  Absorption
Treating (quality improvement)
  Catalytic Reforming
  Isomerisation
  Hydrotreating
Conversion
  Catalytic cracking
  Hydrocracking
  Visbreaking
  Coking
Transformation
  Alkylation
  Etherification

## Slide 5: Demand Shifts Toward Lighter Oil Products
Share of liquid products
Notes: Source: ExxonMobil 2018 Outlook for Energy

## Slide 6: Simplified Fuels Refining
Atmospheric Pipestill – separation by boiling point
Hydrofining – sulfur removal via hydrogen addition
Reforming – increase gasoline octane, chemicals feed for aromatics
Vacuum Pipestill – separation by boiling point under a vacuum
Fluid Catalytic Cracking (FCC) – convert vacuum gas oil to clean products, primarily gasoline
Alkylation – upgrade light ends to high octane gasoline blending components
Hydrocracking – convert vacuum gasoil to clean products, primarily diesel
Coker – convert residual to lighter products and coke
Virgin light ends
Atmos.
Pipe-still
Naphtha Hydrofining
Reformer
Distillate Hydrofining
LPG
Naphtha
Gasoline
Jet Fuel/Kerosene
Distillate/Diesel
Fuel Oil
Crude
Oil
Vacuum Pipe-still
Coker
Gasoline
Jet Fuel/Diesel
Cracked Light
Ends
Gas Oil
Gas
Oil
Light Ends
Asphalt
Fuel Oil
Coke
Low Conversion Refinery
Additional Medium and High Conversion Processing
Additional High Conversion Processing
Alkylation
VGO Hydrocracker
(HDC)
Fluid Catalytic Cracking (FCC)

## Slide 7: Hydroskimming Refinery
Naphtha (10%)
Jet Fuel (10%)
(30%)
(50%)

## Slide 8: Vacuum Distillation Refinery
Naphtha (10%)
Jet Fuel (10%)
5%
25%
35%
20%
30%

## Slide 9
Mogas Production

## Slide 10: Naphtha Streams Before Mogas Processing
Steam Cracker

## Slide 11: Catalytic Reforming
Steam Cracker

## Slide 12: Isomerisation
Steam Cracker

## Slide 13: Alkylation

## Slide 14
Distillates Production

## Slide 15: Hydroskimming Refinery

## Slide 16: Vacuum distillation
Naphtha
Jet Fuel

## Slide 17: Typical Gas Oil Conversion Refinery in Europe

## Slide 18: Hydrocracking Refinery

## Slide 19
Resid Conversion

## Slide 20: Conversion Refinery
Naphtha
CONV

## Slide 21: Residue Conversion Processes
Mild Resid conversion (thermal)
  Visbreaking
Carbon Rejection Processes (thermal)
  Delayed Coking
  Fluid Coking/FLEXICOKING
Hydrogen Addition (Hydroconversion)
  Residfiner
Other Fuel Oil Reduction Steps
  Deasphalting
  Partial Oxidation

## Slide 22: Conversion Processes
Process | Catalyst | H2 | Feed | Carbon dispositioning
FCCU | Yes | No | VGO | CO-CO2
Hydrocracker | Yes | Yes | VGO | HC
Visbreaker | No | No | Resid | HC
Delayed Coker | No | No | Resid | Cokes
FXK | No | No | Resid | CO-CO2
De-asphalter | No | No | Resid | Asphalt
Residfiner | Yes | Yes | Resid | HC

## Slide 23
Sulphur Reduction

## Slide 24: Hydrotreaters in a High Conversion Refinery
Scanfiner

## Slide 25
Back-Up

## Slide 26: Back-up
Fluid Catalytic Cracking unit
Delayed Coker
Visbreaker

## Slide 27: Back-up
Delayed Coker
Solvent Deasphalting unit

## Slide 28: Back-up
Catalytic Cracking unit
Delayed Coker
Flexicoker

## Slide 29: Back-up
Delayed Coker

## Slide 30: Rotterdam Flexicoker